Section 4:  FACILITIES INVENTORY

INSTRUCTIONS:                                                                                                                        OFFICE OF DISABILITY RIGHTS

441 4TH Street, Suite 729 N

Washington, DC 20001

Use this survey checklist to assess the accessibility of District government buildings and other facilities.  Title II of the Americans with Disabilities Act (ADA) requires District government to ensure that its programs, services, and activities are accessible to people with disabilities, including mobility, vision, hearing, and other types of disabilities.

One way of ensuring accessibility is to ensure that the built environment is accessible.  Agencies may use other methods of providing access (such as providing services over the phone, by home delivery, or at curb side) when buildings and facilities are not accessible.  However, an assessment of the physical accessibility of our buildings helps us to identify improvements we can make and to identify what our options are.

The Office of Disability Rights is available to help conduct surveys. For technical assistance and related matters please contact:                    Architect Anwar Mahmood at 202-727-9296 or anwar.mahmood@dc.gov.

Tools:  Office of Disability Rights may be contacted for Information regarding acquisition of survey tools.

- Copies of Survey Forms.  In order to complete the survey, you will need at least one full copy of the survey for each facility.  In most cases, you will need several copies of some of the survey forms for a single facility.  For example, a facility will have more than one entrance, ramp, elevator, door, corridor, room, and toilet room.  Therefore, you will need to make several copies of the needed survey forms.

- Tape Measure

- Door Pressure Gauge

- “Smart Level” which measures slope

- Digital camera

- Clipboard and Pen

- It is helpful to bring 2-3 people to conduct a survey – two persons takes measurements, and one person takes notes

- It is very helpful to have a floor plans of the facilities to be surveyed

Tips:

- Note with as much detail as possible the locations of the elements being measured.

- Take photographs and make notes on the survey forms of the photos of the surveyed elements (for example, on Survey 5-Entrances & Doors, in the “Location” box, provide the location (e.g., Entrance at center of block on 5th Street NW) and state which photos are of that location (e.g., Photos 3-5).

- It is helpful to know when the building was built (relevant dates include before 1973 (Rehabilitation Act), before 1992 (ADA existing building), and after 1992 (ADA new construction) and the dates of any significant alterations.

Note: This questionnaire is a basic survey tool.  It does not include the most detailed requirements of the ADA, but it will help you assess basic accessibility.  For detailed requirements, consult the ADA Accessibility Guidelines, available at http://www.ada.gov/stdspdf.htm.

Some facility elements have additional accessibility requirements that are not addressed in this basic survey instrument, such as parks, play areas, pools, libraries, health care facilities, transportation stations, public rights of way, court rooms, and assembly areas.  Please contact Architect Anwar Mahmood at the Office of Disability Rights (202-727-9296; Anwar.Mahmood@dc.gov) for technical assistance in surveying these types of facilities.

SURVEY   1 -  PARKING

|  | LOCATION: |
| --- | --- |
| Question | ADAAG Requirement / Solution | Yes | No | NA | Measurement |
| Where parking spaces are provided for self-parking, are the required number of accessible parking spaces provided? | 1 to 25 -----------------1 space 26 to 50 ------------- 2 spaces 51 to 75 ------------- 3 spaces 76 to 100 ----------- 4 spaces 101 to 150 --------- 5 spaces 151 to 200 --------- 6 spaces 201 to 300 --------- 7 spaces 301 to 400 --------- 8 spaces 401 to 500 --------- 9 spaces 501 to 1000 ----- 2 % of total 1001 and over ---- 20 plus 1 for each 100 over 1000 (1/6 to be van accessible) |  |  |  | Total number of spaces: _____________________ Number of car accessible spaces: _______________ Number of van accessible spaces: ______________ ______________________________________________________________________________________________________________________________ |
| Is at least 1 per 6 accessible car spaces, van accessible? | 8-foot wide parking space with 8-foot wide access aisle |  |  |  | Parking space width: _____________________ Access aisle width: |
| Are remaining accessible spaces 8 feet wide with a 5-foot access aisle? | 2 spaces may share a single access aisle ____________________________________________________ |  |  |  | Parking space width: __________________________________________ Access aisle width: _____________________ |
| Are the access aisles level [1:50 (2%) slope]? | Curb ramps cannot project into access aisles |  |  |  | Slope: _____________________ |
| Are the access aisles stable, firm and slip resistant? | Access aisles with gravel are not permitted |  |  |  | Type of surface: _____________________ |
| Does each accessible space have a vertical sign showing the International symbol of accessibility? |  |  |  |  | ____________________________________________________________________________________ |
| Does the van accessible space have a vertical “van accessible” sign? | Signs shall be 60” min. AFF to bottom of sign._____________ __________________________ |  |  |  | _______________________________________________________________ |
| Do the van accessible space and the vehicle route to the space have a vertical clearance of at least 98 inches? | ______________________________________________________________________________ |  |  |  | Height of vertical clearance at lowest point: _____________________ |
| Do the access aisles connect to an accessible route? | Route does not require stairs/curbs, and is at least 36 inches wide. Route does not include protruding objects that are not cane detectable. |  |  |  | Width: ____________________________________________________________________________________ _____________________ |
| Are the access aisles closest to the accessible entrance? | ______________________________________________________________________________ |  |  |  | _______________________________________________________________ |

SURVEY  2 -  EXTERIOR ACCESSIBLE ROUTE

|  | LOCATION: |
| --- | --- |
| Question | ADAAG Requirement/Solution | Yes | No | NA | Measurement |
| Is there a route of travel from public transportation, accessible parking, and sidewalks that does not require the use of stairs or un ramped curbs? | __________________________________________________________________________________________________________________________________ |  |  |  | _________________________________________________________________________________________________________ |
| Is the route stable, firm, and slip resistant? | Gravel is not stable, firm and slip resistant |  |  |  | Type of surface: _____________________ |
| Is the route at least 36 inches wide? | The route can narrow to 32 inches (e.g., at doorways) |  |  |  | Width at narrowest point: _____________________ _____________________ |
| Is the running slope of the route lesser than 1:20 [5%] except where ramps are provided? | ______________________________________________________________________________ |  |  |  | Slope at steepest point: _____________________ |
| When the route changes level (e.g., at thresholds), is the vertical difference less than ¼ inch? | Vertical difference up to ½ inch is allowed if the threshold is beveled. Vertical differences greater than ½ inch must be ramped. |  |  |  | Height of level change: __________________________________________ __________________________________________ |
| Is the cross slope of the route level | No greater than 1:50 [2%] |  |  |  | Cross slope at steepest point: |
| Can all objects protruding more than 4 inches into the circulation paths be detected by a blind person using a white cane? | In order to be detected using a cane, an object must be within 27 inches of the ground. Overhead objects must be higher than 80 inches to provide clear head room. |  |  |  | Height of lower edge of protruding objects: ____________________________________________________________________________________ |
| Do all curbs along the route have curb cuts? | Curb cuts must have a slope not greater than 1:12 [8.33%] 1:10 or 1:8 slopes are allowed in pre-1992 facilities with space limitations) |  |  |  | Slope: __________________________________________ _____________________ |
| If the route crosses a vehicular way, are detectable warnings (bumpy domes) provided? | ________________________________________________________________________________________ |  |  |  | _______________________________________________________________ |

SURVEY  3 -  CURB RAMPS

|  | LOCATION: |
| --- | --- |
| Question | ADAAG Requirement/Solution | Yes | No | NA | Measurement |
| Is there a curb ramp wherever an accessible route crosses a curb? | ____________________________________________________ |  |  |  | __________________________________________ |
| Is the slope of the curb ramp 1:12 [8.33%] or less? Slopes up to 1:8 [12.50%] are permitted in pre-1992 facilities with space constraints. | 1:12 [8.33%] means for every 12 inches along the base of the ramp, the height increases one inch. For a 1:12 slope, one foot of ramp length is needed for each inch of height) |  |  |  | Slope: __________________________________________ _______________________________________________________________ |
| Is the curb ramp at least 36 inches wide? | __________________________ |  |  |  | Width: _____________________ |
| Is the transition onto the curb ramp from the top and bottom smooth (without abrupt level changes)? | Level change onto the ramp from the top or bottom should be no more than ½ inch and should be beveled. |  |  |  | Height of level change: __________________________________________ |

SURVEY  4 - RAMPS

|  | LOCATION: |
| --- | --- |
| Question | ADAAG Requirement/Solution | Yes | No | NA | Measurement |
| Are all areas with slopes greater than 1:20 [5%] ramped? | __________________________ |  |  |  | __________________________________________ |
| Are the slopes of ramps lesser than 1:12 [8.33%]? | In pre-1992 buildings, slopes as steep as 1:8 [12.5%] are allowed if there are space limitations. 1:12 means for every 12 inches along the base of the ramp, the height increases one inch. For a 1:12 slope, one foot of ramp length is needed for each inch of height) |  |  |  | Slope at steepest point: __________________________________________ ___________________________________________________________________________________________________________________________________________________ |
| If a ramp is longer than 6 feet, does it have handrails on both sides? | ____________________________________________________ |  |  |  | Length of ramp: _____________________ |
| Are the railings sturdy and 34-38 inches high? | __________________________ |  |  |  | Height:_____________________________________ |
| Does the handrails extend 12” into landings at top & tread depth at bottom. |  |  |  |  |  |
| Is the clear width between the railings at least 36 inches? | __________________________ |  |  |  | Width:_____________________________________ |
| Is the ramp stable, firm and slip resistant? | ______________________ |  |  |  | Type of surface: _____________________ |
| Is a 5-foot long level landing provided at the top and bottom of each ramp? | __________________________________________________________________________________________________________________________________ |  |  |  | Depth of top landing: _____________________ Depth of bottom landing: _____________________ _____________________ |
| Is a 5-foot deep landing provided at any switchbacks? | ______________________________________________________________________________ |  |  |  | Depth of landing: _____________________ Width of landing: _____________________ |
| If the ramp rises more than 30 inches or extends more than 30 feet, is a 5-foot long landing provided? | ______________________________________________________________________________ |  |  |  | Depth of landing: _____________________ |

SURVEY  5 – ENTRANCES & DOORS

|  | LOCATION: |
| --- | --- |
| Question | ADAAG Requirement/Solution | Yes | No | NA | Measurement |
| Are at least 50% of entrances accessible? | __________________________________________________________________________________________________________________________________ |  |  |  | Total number of entrances: ____________________ Number of accessible entrances: _______________ |
| Does each separate tenancy have an accessible entrance? | ____________________________________________________ |  |  |  | __________________________________________ |
| Can each accessible entrance be used independently? | Entrances that require a person to ring a doorbell or wait for staff to open the door are not useable independently. |  |  |  | ____________________________________________________________________________________ |
| If an entrance is not accessible, is directional signage provided directing people to the accessible entrance? | ______________________________________________________________________________ |  |  |  | _______________________________________________________________ |
| If there is a vertical level change between ¼ and ½ inch (e.g., door threshold), is it beveled? | ______________________________________________________________________________ |  |  |  | Height of level change: _____________________ |
| If there is a vertical level change greater than ½ inch, is a ramp, curb ramp, lift, or elevator provided? | ______________________________________________________________________________________________________________________________________________________________________________________ |  |  |  | Height of level change: __________________________________________ Means of access: _______________________________________________________________ |
| At each accessible entrance, does at least 1 of the double leaf doors provide 32 inches clear opening? | With the door open, measure from the face of the door across to the door frame. For double leaf doors, at least one leaf must provide 32 inches clear opening. |  |  |  | Clear width: __________________________________________ _______________________________________________________________ |
| Is there at least 18 inches of clear wall space on the pull side of the door next to the handle? Automatic doors (e.g., push button) are exempt from this requirement. | A person using a wheelchair needs this space to get close enough to open the door and get out of the swing of the door. __________________________ |  |  |  | Clear wall space: __________________________________________ __________________________________________ |
| Is a level landing provided? The required depth of the landing depends on from which direction the door is approached by a wheelchair user. | Check two (pull side and push side) Approach to pull side: ___ Forward approach: 60 inches ___ Side approach to hinge side: 60 inches ___ Side approach to latch side: 48 inches Approach to push side: ___ Forward approach: 48 inches ___ Side approach to hinge side of door: 42 inches ___ Side approach to latch side of door:: 42 inches |  |  |  | Pull side landing depth: __________________________________________ Push side landing depth: __________________________________________ __________________________________________________________________________________________________________________________________________________________________________________________________________________ |
| Is the door handle lower than 48 inches? | ________________________________________________________________________________________________________ |  |  |  | Height: __________________________________________ _____________________ |
| Is the door handle operable with a closed fist? | Round door knobs are not operable with a closed fist. Lever, U-shaped, or push type handles are acceptable. |  |  |  | Shape:_______________________________________________________________________________ |
| How much force is required to open the door? Automatic (e.g., push button) doors are exempt from this requirement. | Interior doors: Required force must be 5 lb or less. Can be measured with a door pressure gauge or a fish scale. |  |  |  | Force to open door: ____________________ __________________________________________ |
| If there are 2 doors in a series, is the clear space between the doors at least 48 inches plus the width of any door that swings into the space? | Doors in a series should either both swing in the same direction or both swing away from the space between the doors. |  |  |  | Distance between doors:________________ Width of door that swings into the space between the doors: _____________________ |

SURVEY   6 -  LOBBIES AND CORRIDORS

|  | LOCATION: |
| --- | --- |
| Question | ADAAG Requirement/Solution | Yes | No | NA | Measurement |
| Does the accessible entrance provide direct access to the main floor, lobby, or elevator? | ______________________________________________________________________________ |  |  |  | __________________________________________ |
| For each floor/level, is there a route that does not require stairs to all public spaces on the floor/level? | __________________________________________________________________________________________________________________________________________________________________________________________________________________________________________ |  |  |  | List public spaces and type of accessible route (e.g., level circulation path, ramp, lift, elevator, stairs) on each floor: ____________________________________________________________________________________ |
| Is the accessible route to all public spaces at least 36 inches wide? | Accessible routes can narrow to 32 inches (e.g., at doorways). |  |  |  | Width at narrowest point: __________________________________________ |
| Is there a 5-foot turning space or T-shaped space for a person using a wheelchair to reverse direction? | ______________________________________________________________________________ |  |  |  | Size of turning area: __________________________________________ |
| If there are 2 doors in a series, is the clear space between the doors at least 48 inches plus the width of any door that swings into the space? | Doors in a series should either both swing in the same direction or both swing away from the space between the doors. ____________________________________________________ |  |  |  | Distance between doors:________________ Width of door that swings into the space between the doors: |
| Can all objects protruding more than 4 inches into the circulation paths be detected by a blind person using a white cane? | In order to be detected using a cane, an object must be within 27 inches of the ground. Overhead objects must be higher than 80 inches to provide clear head room. |  |  |  | Height of lower edge of protruding objects: ____________________________________________________________________________________ |
| If emergency systems are provided, do they have both flashing lights and audible signals? | ______________________________________________________________________________________________________________ |  |  |  | ____________________________________________________________________________________ |

SURVEY  7 - ROOMS AND SPACES

|  | LOCATION: |
| --- | --- |
| Question | ADAAG Requirement/Solution | Yes | No | NA | Measurement |
| Are all aisles and pathways to materials and services at least 36 inches wide? | Accessible routes can narrow to 32 inches (e.g., at doorways). |  |  |  | Width at narrowest point: ____________________________________________ |
| Is there a 5-foot turning circle or T-shaped space for turning a wheelchair completely? | _________________________________________________________________________________ |  |  |  | Size of turning space: ____________________________________________ |
| Is carpeting low-pile, tightly woven, and securely attached along the edges? | ______________________________________________________________________________ |  |  |  | _______________________________________________________________ |
| Can all objects protruding more than 4 inches into the circulation paths be detected by a blind person using a white cane? | In order to be detected using a cane, an object must be within 27 inches of the ground. Overhead objects must be higher than 80 inches to provide clear head room. |  |  |  | Height of lower edge of protruding objects: ______________________ _______________________________________________________________ |
| If emergency systems are provided, do they have both flashing lights and audible signals? | _________________________________________________________________________________ |  |  |  | __________________________________________________________________ |
| Are controls that are available for use by the public located at an accessible height? | For a forward reach, controls must be between 15 and 48 inches high. For a side reach, controls must be between 9 and 48 inches high. |  |  |  | Reach direction (front or side): _____________________ Height: ____________________________________________ |
| Are aisles between seating at least 36 inches wide? | ___________________________ |  |  |  | Width: _____________________ |
| Are the tops of tables or counters between 28 and 34 inches high? | ______________________________________________________ |  |  |  | Height: _____________________ |
| Are knee spaces beneath accessible tables at least 27 inches high, 30 inches wide, and 19 inches deep? | _______________________________________________________________________________________________________________________________________ |  |  |  | Height: _____________________ Width: _____________________ Depth: _____________________ |
| At each type of service counter, is there a portion of the main counter that is at least 36 inches wide and less or equal to 36 inches in height? | This can be addressed by providing an auxiliary counter or folding shelf. ______________________________________________________ |  |  |  | Height: ____________________________________________ Width: _____________________ |
| If check-out aisles are provided, is at least 1 aisle 36” wide and open at all times? | ______________________________________________________ |  |  |  | Width: _____________________ |
| Is the counter at the accessible check-out aisle less or equal to 38” in height? | ________________________________________________________________________________________ |  |  |  | Height: ____________________________________________ |

SURVEY  8 - SIGNAGE

|  | LOCATION: |
| --- | --- |
| Question | ADAAG Requirement/Solution | Yes | No | NA | Measurement |
| Do signs and room numbers designating permanent rooms and spaces meet the following: | _________________________________________________________________________________ |  |  |  | __________________________________________________________________ |
| Mounted with centerline 60 inches from the floor | ______________________________________________________ |  |  |  | Height: ______________________ |
| Mounted on the wall adjacent to the latch side of the door | Signage should not be mounted on the door. ___________________________ |  |  |  | Location: ____________________________________________ |
| Raised characters between 5/8” and 2” high, with high contrast (for room numbers, rest rooms, and exits) | _______________________________________________________________________________________________________________________________________ |  |  |  | Character size: ______________________ Colors (e.g., white on black): |
| Brailed text |  |  |  |  |  |
| If pictograms are used, are they accompanied by text in raised characters and Braille? | _________________________________________________________________________________ |  |  |  | __________________________________________________________________ |
| Do directional and informational signage meet the following: | ______________________________________________________ |  |  |  | ____________________________________________ |
| If mounted above 80 inches, do they have letters at least 3 inches high, with high contrast and non-glare finish? | ____________________________________________________________________________________________________________ |  |  |  | __________________________________________________________________ |

SURVEY  9 - VERTICAL CIRCULATION

|  | LOCATION: |
| --- | --- |
| Question | ADAAG Requirement/Solution | Yes | No | NA | Measurement |
| Are there ramps, lifts, or elevators to all public levels? | __________________________ |  |  |  | ____________________________________________ |
| Stairs: If there are levels that are not served by a ramp, lift, or elevator, do the stairs comply with the following: | ______________________________________________________ |  |  |  | ____________________________________________ |
| Do stair treads have non-slip surface? | __________________________ |  |  |  | ______________________ |
| Do stairs have continuous handrails on both sides, with 12” extensions beyond the top and bottom stairs? | ______________________________________________________ |  |  |  | ____________________________________________ |
| Elevators: Are there both visible and audible door opening/closing and floor level indicators? | _________________________________________________________________________________ |  |  |  | __________________________________________________________________ |
| Are the call buttons in the hallway lower than 42 inches? | ______________________________________________________ |  |  |  | Height: ______________________ |
| Do the controls inside the cab have raised and Braille lettering? | ______________________________________________________ |  |  |  | ____________________________________________ |
| Is there a sign on both door jambs at every floor identifying the floor in raised and Braille letters? | _________________________________________________________________________________ |  |  |  | __________________________________________________________________ |
| If an emergency intercom is provided, is it usable without voice communication? | ______________________________________________________ |  |  |  | ____________________________________________ |
| Is the emergency intercom identified by Braille and raised letters | ______________________________________________________ |  |  |  | ____________________________________________ |
| Lifts: Can the lift be used without assistance? | ___________________________ |  |  |  | ____________________________________________ |
| Is there at least 30 by 48 inches of clear space for a person using a wheelchair to approach to reach the controls and use the lift? | ____________________________________________________________________________________________________________ |  |  |  | Size of clear space: __________________________________________________________________ |
| Are controls between 15 and 48 inches high? | _________________________________________________________________________________ |  |  |  | Height: ____________________________________________ |

SURVEY  10 -  TOILET ROOMS

|  | LOCATION: |
| --- | --- |
| Question | ADAAG Requirement/Solution | Yes | No | NA | Measurement |
| If toilet rooms are provided is each public and common use toilet room accessible? | _________________________________________________________________________________ |  |  |  | __________________________________________________________________ |
| If not all toilet rooms are accessible, is directional signage posted at the inaccessible toilet rooms to direct people to the accessible toilet rooms? | ____________________________________________________________________________________________________________ |  |  |  | ________________________________________________________________________________________ |
| Is the universal symbol of accessibility sign mounted on the wall on the latch side of the door (not on the door) at a height of 60”? |  |  |  |  | Location: ______________________ Height: ________________ |
| If pictograms or symbols are used to identify the toilet room, are raised characters and Braille provided? | _________________________________________________________________________________ |  |  |  | __________________________________________________________________ |
| Are the accessible toilet rooms located on an accessible route (level or ramped or served by an elevator; 36” wide)? | ______________________________________________________________________________ |  |  |  | __________________________________________________________________ |
| Are the accessible fixtures and controls located on an accessible route (level and 36” wide)? | ___ Toilets ___ Urinals ___ Lavatories and mirrors ___ Soap, paper towel, seat cover, and other dispensers ___ Medicine cabinets |  |  |  | Width: ______________________ Width: ______________________ Width: ______________________ Width: ______________________ Width: |
| Are dispensers and controls located lower than or equal to 48 inches in height? | ______________________________________________________________________________ |  |  |  | Height:____________________________________________________________ |
| If a mirror is provided, is the bottom of the reflecting surface lower than or equal to 40 inches from the floor? | Providing a full-length mirror is a good alternative. ____________________________________________________ |  |  |  | Height: ____________________________________________ ______________________ |
| Is there an unobstructed 5-foot turning circle or T-shaped space in the toilet room? | _________________________________________________________________________________ |  |  |  | Size of turning space: ____________________________________________ |
| Do the doors into and within the toilet room (including stall doors) comply with Survey Form 06? | ________________________________________________________________________________________________________________________________________________________________________________________________________________________ |  |  |  | Clear width: ______________________ Clear wall space on latch side: _________________ Weight/opening force: ______________________ Threshold height: ______________________ |
| Is the door handle (including stall doors) operable with a closed fist? | Round door knobs are not operable with a closed fist. Lever, U-shaped, or push type handles are acceptable. |  |  |  | Shape: __________________________________________________________________ |
| Is the door handle lower than or equal to 48 inches from finished floor? | _____________________________________________________________________________________________________________________________________________________________________________________________ |  |  |  | Height: ____________________________________________ ________________________________________________________________________________________ |
| Toilets: Is there a wheelchair accessible stall with an area at least 5 feet by 5 feet outside the door swing? OR Is there a stall that is 59” by 60” outside the door swing? OR Is there a stall with wall hung toilet that is 56” by 60” outside the door swing? OR Is there an ambulatory stall that is 35”-37” by 60” outside the door swing? | ______________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________ |  |  |  | Size of clear floor space: ____ X ____ Size of stall: ____ X ____ ______________________________________________________________________________________________________________ |
| In the accessible stall, is there a grab bar 36 inches long and 33-36 inches high behind the toilet? | ____________________________________________________________________________________________________________ |  |  |  | Length: ____________________________________________ Height: ______________________ |
| In the accessible stall, is there a grab bar at least 42 inches long and 33 to 36 inches high on the side wall closest to the toilet? | __________________________________________________________________________________________________________________________________ |  |  |  | Length: ______________________ Height: ______________________ |
| Is the toilet seat 17-19 inches high? | ___________________________ |  |  |  | Height: ______________________ |
| Is the toilet paper dispenser below the side grab bar and at least 19 inches high? | _________________________________________________________________________________ |  |  |  | Height: ______________________ Location: |
| Is the center of the toilet 16 to 18 inches from the side wall with the grab bar? | ____________________________________________________ |  |  |  | Distance: ______________________ |
| If there is a lavatory in the stall, is the edge of the lavatory at least 18 inches from the centerline of the toilet? | ____________________________________________________________________________________ |  |  |  | Distance: ____________________________________________ ______________________ |
| Urinals: Does at least one urinal has an elongated rim lower than or equal to 17 inches high? | ____________________________________________________________________________________________________________ |  |  |  | Rim height: ____________________________________________ ______________________ |
| Is there a clear floor space 30” wide and 48” long which allows a forward approach to the urinal? | ____________________________________________________________________________________________________________ |  |  |  | Width: ____________________________________________ Length: ______________________ |
| Lavatories: Is at least one accessible lavatory? | ______________________________________________________ |  |  |  | ____________________________________________ |
| Is the lavatory rim/counter lower than or equal to 34 inches in height? | _________________________________________________________________________________ |  |  |  | Height to top of lavatory/cabinet: ______________________ ______________________ |
| Is there knee clearance under the sink at least 29 inches high below the lavatory? | Enclosed cabinetry under the sink is not acceptable. ___________________________ |  |  |  | Height to bottom of lavatory/cabinet: ______________________ ______________________ |
| Is the front edge of the lavatory at least 17 inches from the wall? | ______________________________________________________ |  |  |  | Distance: ______________________ |
| Is there a clear floor space at least 30” wide and 48” long which allows a forward approach to the lavatory? | Does the clear space extend up to 19” under the lavatory? ________________________________________________________________________________________ |  |  |  | Width: ____________________________________________ Length: ______________________ |
| Are the hot water pipes insulated or wrapped to prevent contact? | __________________________________________________________________ |  |  |  | __________________________________________________________________ |
| Can the faucet be operated with a closed fist? | Round knobs are not acceptable (lever, push-button, or paddle handles are acceptable) |  |  |  | ______________________________________________________________________________________________________________________________ |
| If shelves or coat hooks are provided, are they reachable by a wheelchair user? | Shelf / hook maximum allowed height is 48” |  |  |  | Height: ____________________________________________ ____________________________________________ |

SURVEY 11 - BATHING FACILITIES

|  | LOCATION: |
| --- | --- |
| Question | ADAAG Requirement/Solution | Yes | No | NA | Measurement |
| Are bathing facilities located on an accessible route (level or ramped, 36” wide)? | ________________________________________________________________________________________________________________ |  |  |  | Height of level change: ______________________ Width: ______________________ |
| Do the doors into and within the bathing room comply with Survey Form 06? | ____________________________________________________________________________________________________________________________________________________________________________________________________ |  |  |  | Clear width: ______________________ Clear wall space on latch side: _________________ Weight/opening force: ______________________ Threshold height: ______________________ |
| Is the door handle operable with a closed fist? | Round door knobs are not operable with a closed fist. Lever, U-shaped, or push type handles are acceptable. |  |  |  | Shape: ____________________________________________ ______________________ |
| Is the door handle lower than or equal to 48 inches in height? | ______________________________________________________ |  |  |  | Height: ______________________ |
| Does at least one shower or tub comply with the requirements below? | ________________________________________________________ |  |  |  | ____________________________________________ |
| Showers: |  |  |  |  |  |
| If shelves or coat hooks are provided, are they reachable by a wheelchair user? | Shelf / hook maximum allowed height is 48”. |  |  |  | Height: ____________________________________________ |
| Is there a clear floor space outside the shower at least 36” by 48”, with 12” extending beyond the seat wall? | ________________________________________________________________________________________________________________ |  |  |  | Width: ____________________________________________ Length: ______________________ |
| Is the shower stall exactly 36” by 36”? | ____________________________________________________________________________________ |  |  |  | Width: ______________________ Length: |
| Is there an L-shaped seat mounted 17-19 inches high? | ______________________________________________________ |  |  |  | Height: ______________________ |
| Is the seat on the wall opposite the controls? | ___________________________ |  |  |  | ______________________ |
| Are grab bars provided on the control wall and the side wall (not behind the seat)? | _________________________________________________________________________________ |  |  |  | ____________________________________________ |
| Are the grab bars 33-36 inches high? |  |  |  |  | Height: ______________________ |
| If there is a curb at the entrance to the shower, is it lesser than ½ inch in height? | ________________________________________________________ |  |  |  | Height:______________________________________ |
| Are the controls operable with a closed fist? | Round controls are not acceptable |  |  |  | ____________________________________________ |
| Is a shower hose provided? | ____________________________ |  |  |  | __________________________________________ |
| Roll-in Showers: |  |  |  |  |  |
| Is there a clear floor space beside the shower at least 36” by 60”? | ____________________________________________________________________________________ |  |  |  | Width: ______________________ Length: ______________________ |
| Is the shower enclosure at least 36” by 60”? | ________________________________________________________ ____________________________ |  |  |  | Width: ______________________ Length: _____________________ |
| Are there grab bars on 3 sides? | ____________________________ |  |  |  | __________________________________________ |
| Is there no curb into the shower? | ____________________________ |  |  |  | __________________________________________ |
| Are the controls located on the back wall? | ______________________________________________________ |  |  |  | ____________________________________________ |
| Are the controls operable with a closed fist? | Round knob controls are not acceptable. __________________ |  |  |  | __________________________________________________________________ |
| Is a shower hose provided? | ____________________________ |  |  |  | __________________________________________ |
| Bathtubs: |  |  |  |  |  |
| Is there a clear floor space at least 30” wide by 60” long beside the tub? | ____________________________________________________________________________________ |  |  |  | Width: ______________________ Length: ______________________ |
| Is a fixed or removable seat provided? | ________________________________________________________ |  |  |  | __________________________________________________________________ |
| Are grab bars provided as follows: 1 grab bar at the control end of the tub 2 grab bars on the long side wall of the tub 1 grab bar at the seat end of the tub | _____________________________________________________________________________________________________________________________________________________________________________________________ |  |  |  | Locations: ____________________________________________ __________________________________________________________________ |
| Are controls operable with a closed fist? | Round knob controls are not acceptable. ________________ |  |  |  | ____________________________________________ |
| Is a shower hose provided? | ____________________________ |  |  |  | __________________________________________ |

SURVEY 12 -  WATER FOUNTAINS

|  | LOCATION: |
| --- | --- |
| Question | ADAAG Requirement/Solution | Yes | No | NA | Measurement |
| Is there at least 1 water fountain with clear floor space of at least 30” by 48” in front? | ________________________________________________________________________________________________________________ |  |  |  | Width: ______________________ Length: ______________________ |
| Does that fountain have its spout lower than or equal to 36” in height? | ________________________________________________________ |  |  |  | Spout height: ______________________ |
| Are the controls mounted on the front or side? | ____________________________________________ |  |  |  | ____________________________________________ |
| Are the controls operable with a closed fist? | Round knobs are not acceptable. __________________________ |  |  |  | _____________________________________________ |
| Is another water fountain mounted at a standard height for standing people? | ________________________________________________________ |  |  |  | ____________________________________________ |
| Are all water fountains detectable by a blind person using a white cane? | ___ Bottom extends to less than 27” above the floor OR ___ post or cane detectable barrier should be provided OR ___ recessed in an alcove |  |  |  | __________________________________________________________________________________________________________________________________________________________ |

SURVEY 13 - PUBLIC TELEPHONES

|  | LOCATION: |
| --- | --- |
| Question | ADAAG Requirement/Solution | Yes | No | NA | Measurement |
| Does at least one phone have a clear floor space at least 30” by 48” in front? | ____________________________________________________________________________________ |  |  |  | Width: ______________________ Length: |
| Is the highest operable part of the phone lower than or equal to 48” in height? | 48” is permitted if a side approach is possible. |  |  |  | Height: ______________________ |
| Is the phone detectable by a blind person using a white cane? | ___ Projects no more than 4” into circulation path OR ___ bottom edge no more than 27” above the floor OR ___ pole or cane detectable barrier provided OR ___ recessed in an alcove |  |  |  | ____________________________________________________________________________________________________________________________________________________________________________________________________________________________ |
| Does the phone have push-button controls? | ________________________________________________________ |  |  |  | ____________________________________________ |
| Is the phone hearing-aid compatible? | ________________________________________________________ |  |  |  | ____________________________________________ |
| Does the phone have volume control? | ________________________________________________________ |  |  |  | ____________________________________________ |
| If there are 4 or more public phones in the building, is a text telephone (TTY or TDD) provided? | ____________________________________________________________________________________ |  |  |  | __________________________________________________________________ |
| Is the location of the TTY or TDD identified by signage with the International TTY symbol? |  |  |  |  | ________________________________________________________________________________________ |

SURVEY 14 - SELF SERVICE MACHINES (VENDING & ATM)

|  | LOCATION: |
| --- | --- |
| Question | ADAAG Requirement/Solution | Yes | No | NA | Measurement |
| If ATMs or vending machines are provided, is there a clear floor space in front of the machine at least 30” by 48”? | __________________________________________________________________________________________________________________________________ |  |  |  | Width: ______________________ Length: ______________________ |
| At ATM machines, are all operable parts lower than or equal to 48” in height? | If only a forward approach is possible, maximum height is 48”. __________________________ |  |  |  | Height: ______________________ |
| At ATM machines, are instructions provided in Braille or by audio? | _________________________________________________ ____________________________________________________________________________________ |  |  |  | ________________________________________________________________________________________ |

SURVEY 15 - RESTAURANTS AND CAFETERIAS

|  | LOCATION: |
| --- | --- |
| Question | ADAAG Requirement/Solution | Yes | No | NA | Measurement |
| If food/drinks are served at counters or bars, is 60" portion of the counter lower than or equal to 34” in height? | ____________________________________________________________________________________ |  |  |  | Height: ____________________________________________ |
| Does the accessible portion of the counter provide knee space underneath that is at least 27” high, 30” wide, and 19” deep? | Alternately, can provide table service at accessible tables located nearby. ________________________________________________________________________________________________________ |  |  |  | Height: ______________________ Width: ______________________ Depth: ______________________ |
| Are at least 5% of tables 28” to 34” high? | ________________________________________________________ |  |  |  | Height: ______________________ |
| Are food service lines at least 36” wide? | ________________________________________________________ |  |  |  | Width: ______________________ |
| Are tray slides at food service lines lower than or equal to 34” in height? | ________________________________________________________ |  |  |  | Height: ______________________ |
| If self-service shelves are provided, are at least 50% lower than or equal to 48” in height? | If only a front approach is possible, maximum height is 48”. ____________________________ ______________________ |  |  |  | Height: ____________________________________________ |

OTHER FACILITIES

Please list below any facilities that were not surveyed or for which you could not find an applicable requirement in the survey forms:

________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________

____________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________

____________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________